## Slide 1: Mobile Sensors Workshop, Part 2: Digital
Pierce Nichols
15 February 2015

## Slide 2: Analog to Digital Conversion
The ADC measure the signal at regular intervals.
Ideally, it measures it at discrete times.
Sample rate is the number of samples per second.
Resolution is the number of bins, expressed in bits (powers of two)

## Slide 3: Quantization
ADC output can only assume a discrete number of values…
The difference between the real signal and your measured signal shows up as noise or error.
Minimized by using sufficiently high resolution ADC.

## Slide 4: Aliasing
Since we’re only measuring at discrete times, it’s possible to get fooled.
Higher frequency signals can masquerade as lower frequency signals.
No way to tell the difference post sampling.
Notes: Break out the one_channel_scope code and the function generator to demonstrate this.

## Slide 5: Fourier’s Theorem
All time varying signals can be expressed as a sum of sine waves of varying frequency, amplitude, and phase.
This means we can take a signal and express it in terms of the frequencies of the sine waves that make it up.
If this wasn’t true, the Internet wouldn’t work.

## Slide 6: Nyquist-Shannon Sampling Theorem
If a signal x contains no frequencies higher than B Hz, it is completely determined by giving its value at a series of points spaced 1/(2B) seconds apart.
In order to accurately sample a signal, we need to exclude signals with a frequency greater than half of the sampling frequency.
Some signals we can trust don’t exceed half of the sampling frequency…
But mostly we filter higher frequencies out.

## Slide 7: The RC (resistor-capacitor) filter
A resistor-capacitor is the simplest sort of filter.
The equivalent resistance of the capacitor is frequency dependent
This functions as a frequency-dependent voltage divider.
This is a low-pass filter; swapping the components makes a high-pass filter.

## Slide 8: Sizing the RC filter
The corner frequency of a filter is the point at which it attenuates the signal power by a factor of 2 (3 dB)
, where the frequency is in hertz, R is in ohms, and capacitance is in farads
Signal power is attenuated by 20 dB/decade above .
If we put additional RC filters in series, we can increase the attenuation by 20 dB/decade per capacitor.
Each capacitor (or inductor) is called a pole. So a two capacitor filter is a 2-pole filter.

## Slide 9: Example calculation
R = 100 kΩ
C = 100 nF

## Slide 10: A quick note on decibels (dB)
The decibel is a logarithmic unit for expressing ratios
10 dB is one order of magnitude (x10) when measuring power
20 dB is one order of magnitude when measuring voltage or amplitude, since power is usually proportional to the square of amplitude
Decibels used to measure things like sound power and output power are based on some reference level
  Sound in air, 1 dB = 20 micropascals
  Sound in water, 1 dB = 1 micropascal
  RF output, 1 dB = 1 mW

## Slide 11: Calculating dB
For power:
For amplitude:
Since (Ohm’s Law), these give the same values for the same circuit.
3 dB (power) is a factor of 2
10 dB (power) is a factor of 2

## Slide 12: More advanced filters…
It is possible to make a multi-pole filter with a passband gain of 1 (or higher) by adding op-amps to the mix.
A Sallen-Key filter gives two poles per op-amp
A Biquad filter can, with proper passive selection, replicate any continuous filter function.
Typical modern practice is to minimally filter the signal, oversample enormously, and then do all remaining filtering digitally.

## Slide 13: Ten minute break…

## Slide 14: Digital sensors
Digital sensors are sensors that have the sensor, signal conditioning, ADC, and perhaps some post-processing integrated into a single device.
Digital sensors communicate with the rest of your system over some sort of digital link rather than by voltage or current.
External ADCs are also available and communicate like digital sensors.

## Slide 15: Digital logic
Digital logic consists of ones and zeros, corresponding to high and low voltage levels.
Arduino is a bit more robust than this.

## Slide 16: Arduino digital levels
Arduino levels are a bit different than standard TTL or CMOS.
Interoperable with 3.3V CMOS as long as absolute maximums not exceeded.

## Slide 17: Digital busses for sensors
TTL Serial – Simple, implemented in hardware on nearly every µC. One wire for each direction plus ground.
Serial Peripheral Interface (SPI) – Widely implemented in hardware, speeds to ten of megabits/sec, good noise resistance. Requires three wires, ground, and one select line per device on multi-drop busses. Good noise immunity, fast.
Parallel – One wire per bit plus ground and a clock/latch line. Extraordinarily fast.
Inter-IC (I2C) – Two wires (SDA & SCL) plus ground. 7-bit addresses, so up to 112 devices on a single bus. Not very fast and questionable noise immunity, but very common.

## Slide 18: I2C Properties
Leader-follower bus architecture. One device (the Arduino in our case) is the leader, and all other devices follow.
SDA (data) and SCL (clock) lines are pulled up to Vcc by pull-up resistors.
Active state (the one) of each line is ground.
Typical clock frequency is 100 kHz
High speed mode (supported by Atmega328P but not Arduino) is 400 kHz.
Leader mode supported by Arduino Wire library.

## Slide 19: I2C Connections

## Slide 20: I2C component selection
Minimize series resistances (Rs)
Pull-up resistors 2kΩ – 10kΩ. Smaller resistors for longer wires/faster speeds.
Minimize parasitic capacitance between wires (Cc)
Parasitic capacitance between wires and ground (Cp) must be less than 400 pF
Longer lines = higher parasitic capacitance!

## Slide 21: I2C communications

## Slide 22: Ten minute break…

## Slide 23: 9-DoF IMU (
Nine degrees of freedom inertial measurement unit
  3 axis accelerometer
  3 axis rate gyroscope
  3 axis magnetometer (compass)
All sensors communicate I2C
Cheap sensors enabled by cell phone requirements

## Slide 24: Wiring up the IMU

## Slide 25: Libraries required
Move the following directories from the Arduino/libraries directory in the class files to your Arduino/libraries directory.
  Adafruit_Sensor
  Adafruit_LSM9DSO
  Adafruit_AHRS

## Slide 26: Opening the ‘tester’ example sketch

## Slide 27: Start of the code…

## Slide 28: Setup…

## Slide 29: Grabbing & printing the data

## Slide 30: Open the ahrs_9dof example

## Slide 31: AHRS (attitude & heading reference system) startup code

## Slide 32: Grabbing the data…

## Slide 33: Euler angles
Angles around the axes
Roll is around X axis, pitch is around Y axis, and yaw is around Z axis
Order is important!
Z axis points down so positive yaw angle has the same sense as a compass.

## Slide 34: Limits of the Adafruit AHRS code
Doesn’t incorporate gyro data
Assumes that the acceleration vector always points down
Doesn’t fix the data rate as a constant
Magnetometer & accelerometer need calibration for best performance.

## Slide 35: One last device (not really a sensor)
Each kit also contains a near IR receiver
Demodulates remote control signals (38 kHz modulation)

## Slide 36: Source for parts & kits
Local
Ada’s Technical Books
Vetco
Alphatronics
Fry’s Electronics
Metrix Create Space
Online
Digikey (www.digikey.com)
Mouser (www.mouser.com)
Sparkfun (www.sparkfun.com)
Adafruit Industries (www.adafruit.com)
Solarbotics (www.solarbotics.com)
Makershed (www.makershed.com)

## Slide 37: Books
Electronics
Make: Electronics (Platt)
Engineer’s Mini Notebooks Vol 1 – 4 (Mims)
The Art of Electronics 2nd Ed (Horowitz & Hill)
Circuit Design: know it all (Ashby et al)
Arduino Cookbook (Margolis)
Data Analysis
The Statistical Analysis of Experimental Data (Mandel)
Sensors
Handbook of Modern Sensors (Fraden)
AHRS & Euler Angles
Physics for Game Developers (Bourg)

## Slide 38: Online learning resources
Sparkfun (learn.sparkfun.com)
Adafruit (learn.adafruit.com)
Arduino Playground (playground.arduino.cc)
Arduino Forum (forum.arduino.cc)
Arduino Reference (arduino.cc/en/Reference/HomePage)
Wikipedia